# Typical Specifications

Series CSB – Furnish and install directly on the discharge side of each pump a PACO Series PSD Combination Value incorporating three functions in one body: non-slam check, positive shut-off, and flow balancing (throtting). Valve shall be cast iron with bronze disc, stainless steel stem and spring. Connections shall be 125# ANSI flanges. Valve shall incorporate an O-ring seat to assure soft, positive, non-slamming value closure. Valve body shall have two threaded port connections on each side of the value seal for measurement purposes. A separate drainage port shall be provided. Valve shall include a visual indicator valve positioning (percentage open) and shall incorporate a memory device to promote simplified return of valve to propped balance following valve closure.